## Slide 1: MARS
A Brief Introduction
Computer Organization

## Slide 2: Outline
Download and Install
The Interface of MARS
MIPS assembly instructions
System calls
A Simple Example

## Slide 3: Download and Install MARS
Where to download
  https://courses.missouristate.edu/KenVollmar/mars/MARS_4_5_Aug2014/Mars4_5.jar
We use MARS as our MIPS simulator
Cross-platform: Linux, Mac OS X, or Windows

## Slide 4: Interface of MARS
Messages
Registers
Text

## Slide 5: Window Interface
Registers
  Display all the values stored in the available registers of a
MIPS CPU
Text
  Show instructions and addresses
  Including system subroutine and the code
Messages
  Show messages (including error messages)

## Slide 6: Simulator Functions

## Slide 7: Basic MIPS Instruction Set
MIPS instructions
Name
Add
add
Subtract
sub
Add immediately
addi
Load word
lw
Store word
sw
Load byte
lb
Store byte
sb
Load upper immediately
lui
Branch on equal
beq
Branch on not equal
bne
Set less than
slt
Set less than immediately
slti
MIPS instructions
Name
Jump
j
Jump register
jr
Jump and link
jal
Move
move
Multiply
mult
Multiply immediately
multi
Load immediately
li
Branch less than
blt
Branch less than or equal ble
Branch greater than
bgt
Branch greater than or equal
bge

## Slide 8: MIPS Register Table

## Slide 9: MIPS Register Table
Type | Name | Number | Usage
Assembler related | $at | $1 | Preserved for assembler
OS related | $k0 - $k1 | $26 - $27 | Preserved for OS
Procedure call | $v0 - $v1 $a0 - $a3 $ra | $2 - $3 $4 - $7 $31 | Values for results Arguments Return address
Memory management | $gp $sp $fp | $28 $29 $30 | Global pointer Stack pointer Frame pointer
Variables / constants | $s0 - $s7 $t0 - $t7 $t8 - $t9 $zero | $16 - $23 $8 - $15 $24 - $25 $0 | Saved Temporaries More temporaries The constant value 0

## Slide 10: System Services Table (part)
Service | System Call Code | Arguments | Result
print_int | 1 | $a0 = integer | 
print_float | 2 | $f12 = float | 
print_double | 3 | $f12 = double | 
print_string | 4 | $a0 = string | 
read_int | 5 |  | integer (in $v0)
read_float | 6 |  | float (in $f0)
read_double | 7 |  | double (in $f0)
read_string | 8 | $a0 = buffer, $a1 = length | 
sbrk | 9 | $a0 = amount | address (in $v0)
exit | 10 |  | 
print_character | 11 | $a0 = character | 
read_character | 12 |  | character (in $v0)

## Slide 11: System Call
Example
– Read an integer (user input)
#assign a system call type
#execute system call
li $v0, 5
syscall
– Print a string
# assume that ‘msg’ represents a string
li $v0, | 4 | # | system call code for print_str
la $a0, | msg | # | load address of ‘msg’ into $a0
syscall |  | # | print the string

## Slide 12: Data Types
Data Types
  .word, .half - 32/16 bits integer
  .byte - 8 bits integer (similar to ‘char’ type in C)
  .ascii and .asciiz - string (asciiz is null-terminated)
    .asciiz is preferable (for C-based machines)
    Strings are enclosed in double-quotas(”)
    Special characters in strings follow the C conventions
– newline(\n), tab(\t), quote(\”)
  .double, .float - floating point

## Slide 13: MIPS Assembler Directives
Other Directives
  .text - Indicates that following items are stored in
the user text segment
    Code zone!
  .data - Indicates that following data items are
stored in the data segment

## Slide 14: MIPS Assembly Layout
Program layout
.text # code section main: # user program code
.data # data section Label_1: .data_type list_of_data # data loc + data type + data
.text # code section Label_2: # function label # user functions

## Slide 15: Example for data
Initialize data
.data
i: .word 10 # initialize a word
a: .word 0, 0, 0 # initialize an array
b: .word 0:3 # the same as array1
.text
lw $t0, i

## Slide 16: Call Function (jal)
Call function
main: # main function
… # code
jal function_label # call a function
…
function_label:
… # code
jr $ra # back to main

## Slide 17: Call Function (bne , beq…)
Call function
main: # main function
… # code
beq $s0,$zero function_label
# call a function if $s0 = 0
…
function_label:
… # code
jr $ra # back to main

## Slide 18: The Stack
The stack grows from high addresses to low addresses
Stack Pointer ($sp)

## Slide 19: The Stack
push: addi $sp, $sp, -4
# Decrement stack pointer by 4
  sw $t0, 0($sp)
  # Save $t0 to stack
pop: lw $t0, 0($sp)
# Copy from stack to $t0
addi $sp, $sp, 4
# Increment stack pointer by 4

## Slide 20: Demo

## Slide 21: Thank you for your attention